## Slide 1
Learn about… Using CAD with Digimap data
Ian Holmes and Guy McGarva
EDINA Geoservices Support
15 November 2017

## Slide 2: Follow-up
After the webinar, we will send you links to:
Webinar Recording (YouTube)
Slides
Transcript of all Questions and Answers
Feedback form

## Slide 3
Datasets available in CAD format
How to access the data
Using the data in AutoCAD
Content

## Slide 4: Poll
What is your current status at your institution?
Undergraduate
Postgraduate
Support staff
Academic staff
Other

## Slide 5: What data is available in CAD format?
http://bit.ly/OS_Formats
Vector datasets | CAD formats
MasterMap Topography Layer Standard - full colour style Plan - outline style | DWG
MasterMap Sites Layer | DWG
MasterMap Building Height Attribute (BHA) | DWG
VectorMap Local | DWG
Strategi | DXF
Meridian 2 | DXF

## Slide 6: OS MasterMap Topography Layer
Most detailed mapping from OS
Good for large scale projects covering small areas
Fully polygonised covering the whole of GB
Maps the type of features found on the ground
Two flavours:
  Full colour (polygons)
  Plan/outline (line work)
MasterMap Topogaphy Layer (DWG format)
© Crown Copyright and Database Right 2017. Ordnance Survey (Digimap Licence)

## Slide 7: Building Height Attribute
Released by OS in March 2014
Last updated December 2014
Alpha release – no guarantee error free
Incomplete coverage, currently only major towns and cities: http://bit.ly/BuildingHeightsCoverage
In future will be included in Topography layer
© Crown Copyright and Database Right 2017. Ordnance Survey (Digimap Licence)

## Slide 8: Building Height Attribute
Base height: AbsHMin
‘Roof’ height: AbsH2
All attributes included as Xdata
Need to use with a DTM surface otherwise buildings will be floating in mid air

## Slide 9: VectorMap Local data
Designed for display at 1:10,000 scale
Good for smaller scale, town level projects
Includes contours and spot heights
© Crown Copyright and Database Right 2017. Ordnance Survey (Digimap Licence)
VectorMap Local (DWG format)

## Slide 10: What data is available in CAD format?
http://bit.ly/OS_Formats
Height (terrain) datasets | CAD formats
Terrain 5 DTM | ASC and XYZ
Terrain 5 Contours | DWG
Terrain 50 DTM | ASC
Terrain 50 Contours | SHP or GML
*Land-Form PROFILE DTM and contours | DXF
*Land-Form PANORAMA DTM and contours | DXF
* Land-Form PROFILE and PANORAMA have been withdrawn by Ordnance Survey and are no longer updated.

## Slide 11: Height Data
Various Raster (DTM) and Vector (contour) datasets available:
Terrain 5
  Contours at 5 metre interval
  DTM with 5m cell size
Terrain 50
  Contours at 50m interval [not available in native CAD format]
  DTM with 50m cell size
Land-Form PROFILE [DXF] – withdrawn by OS
Land-Form PANORAMA [DXF] – withdrawn by OS
Terrain 50 Contours
Terrain 50 DTM
© Crown Copyright and Database Right 2017. Ordnance Survey (Digimap Licence)
© Crown Copyright and Database Right 2017. Ordnance Survey (Digimap Licence)

## Slide 12: What data is available in CAD format?
http://bit.ly/OS_Formats
Backdrop mapping | CAD formats
MasterMap Topography Layer Raster | TIFF
VectorMap Local Raster | TIFF
1:25,000 Colour Raster | TIFF
1:50,000 Colour Raster | TIFF
VectorMap District Raster | TIFF
Aerial imagery | JPEG

## Slide 13: Backdrop mapping
10 products available
Raster maps – useful as backdrop
All in TIFF image format
Largest scale is raster version of MasterMap Topography Layer at 1:1,000
Smallest scale is MiniScale at 1:1,000,000
1:25,000 Colour Raster
© Crown Copyright and Database Right 2017. Ordnance Survey (Digimap Licence)

## Slide 14: Aerial Imagery
25cm resolution vertical aerial imagery
JPEG format
Various fly dates
Aerial imagery with buildings from OS MasterMap
© Getmapping Plc
© Crown Copyright and Database Right 2017. Ordnance Survey (Digimap Licence)

## Slide 15: Update Frequency
Digimap > OS Help > Data Information > Data update dates
http://bit.ly/OSUpdates

## Slide 16: Where do I get the data?
Ordnance Survey > Data Download
Download OS mapping data for use in GIS/CAD

## Slide 17: Data Download
All available OS map data
Download several map products in one order
5 categories of map data
3 steps to order map data

## Slide 18: Using Data Download
Three step process:
Select area
Choose data
Add to basket
  Options to change format, version and layers
Notes: It’s straightforward to use Data Download – ordering map data involves 3 steps:
Select your area on the map – there are 4 methods for selection. The shaded orange area you see here is our selected area.
Select the map data that you wish to download. You can open any category of map data by clicking on the name. Then it’s a matter of ticking the box next to any map data you wish to download. You can download as many as you like in an order, provided you do not exceed the allowances. There is an allowance for each map data product – in order that our servers can process orders as quickly as possible.
Third step is to add to basket. Once you click the add to basket button, your basket pops up on screen. You can then select from different formats, date versions and map layers, where available. Options will different depending on map product.

## Slide 19: Basket options
Dataset options:
Version – dataset version as released by Ordnance Survey
Format – note different datasets available in different formats
Theme – some datasets are available in different styles e.g. full colour and line drawing
Layers – use this to download some features from the full dataset, e.g. just building features from OS MasterMap Topography Layer

## Slide 20: Poll
What software do you use regularly with map data? Tick ALL that apply.
AutoCAD
AutoCAD Map 3D
VectorWorks
ArcGIS
Other

## Slide 21: How do I use the data?
Viewing MasterMap Topography Layer
  Two styles: full colour and plan/outline
  Attributes stored as Extended Attribute Data (Xdata)
Viewing MasterMap Building Height Attribute
  Buildings floating in mid air
  Attach Terrain 5 contours
Lots of work done to ensure all datasets align correctly
  All data in British National Grid
  All data uses metres as unit of measurement
3D visualisation with Building Height Attribute in InfraWorks

## Slide 22: Add OS MasterMap topography to AutoCAD
DWG format:
  Will open directly in AutoCAD products
  Includes default OS representation
  Attributes stored as Extended Attribute Data (Xdata), which is not easy to interrogate
GML format:
  Can be imported in to AutoCAD
  Minimal representation
  Control over which features are imported
  More detailed attribute analysis possible
  Can control the order in which layers are drawn

## Slide 23: 3D visualisation with Building Height Attribute (BHA)
Download the following from Digimap:
  Building Height Attribute in DWG format;
  DTM surface (e.g. Terrain 5 or Terrain 50);
  Any other backdrop mapping as required (e.g. Aerial Imagery or MasterMap Raster).
Can be viewed in a variety of packages including AutoCAD Map 3D or InfraWorks.

## Slide 25: Recent developments
OS Terrain 5 DTM in XYZ format
Standardised all DWG data to use British National Grid so that they overlay correctly
Release of Aerial Digimap
Release of Lidar Digimap
If there is anything you would like to see added to the service, please send your suggestions to edina@ed.ac.uk!

## Slide 26: Resources
Digimap Resource centre: http://digimap.edina.ac.uk/webhelp/resources/index.html

## Slide 27: AutoCAD pages

## Slide 28: Questions?